CIVIL ENGINEERING PROBLEM.

An engineer is given the task of working out the cheapest way to construct a road across a swampy area joining two existing roads on either side.

Existing road

HARD GROUND

C

SWAMPY LAND                                    80 m

A                             B

Existing road                             Proposed road                   x

HARD GROUND                           200 m

The cost of building a road on hard ground is $1000 per metre and the cost on swampy ground is $3000 per metre.

Solution:

Distance AB = 200 – x     and (by Pythag) distance BC = √(802 + x2)

Cost C =  AB×$1000 + BC×$3000

=  (200 – x)×1000 + √(802 + x2) × 3000

= 200000 – 1000x + √(802 + x2) × 3000

The MINIMUM cost will be when  dC = 0

dx

dC =   – 1000 +    1 × 2x  × 3000              =     0

dx                         2√ (802 + x2)

so                       3000x                          =     1000

√ (802 + x2)

3x                 = √ (802 + x2)

9x2                =    802 + x2

8x2               =    802

x                =   28 metres (rounded to the nearest metre)

(In this case it is probably easier to consider the gradient on either side of x = 28 instead of doing the 2nd derivative test.

At x = 27,  C ' = negative                      and at x = 29,  C ' = positive   so there is a MIN at x = 28)

So Minimum cost = 200000 – 1000x + √(802 + x2) × 3000

= 200000 – 1000×28 + √(802 + 282) × 3000

= $426,000